## Slide 1: Corsair One i500 BIOS Update SOP

## Slide 2: Required Components
USB Disk with FAT32 file system
BIOS for Corsair One i500
  You can download the BIOS package from Corsair Website

## Slide 3: Caution
Please extract the BIOS-zip file that you have downloaded and store it to your USB storage device
Please DO NOT shutdown or restart system until BIOS update process is completed

## Slide 4: Step 1. Entering to BIOS menu
Boot up your system & press “Delete” key to enter BIOS menu to check your current BIOS version.

## Slide 5: Step 2. M-flash for BIOS update
2.2 select “M-Flash”. You can find M-Flash Button in both BIOS EZ Mode and BIOS Advance Mode.
BIOS EZ mode
BIOS Advanced mode

## Slide 6: Step 2. M-flash for BIOS update
2.2 After selecting “M-Flash”, a notification will appear telling you the system will automatically reboot and enter flash mode. Press “Yes” to continue.

## Slide 7: Step 3. Perform BIOS update
3.1 Select USB storage device and file path with the downloaded BIOS.
3.2 Select the BIOS which you want to update and press “Enter” to start updating.
Note 1: You can double check the Current BIOS version and the Selected BIOS version at the bottom of the screen.
Note 2: If you cannot see the BIOS in M-Flash, please double check if the downloaded BIOS is correct

## Slide 8: Step 3. Perform BIOS update
3.3 A notification will appear to confirm if you have selected the correct BIOS file.
Press “Yes” to start updating.
Press “No” if you have noticed the BIOS file is not correct

## Slide 9: Step 3. Perform BIOS update
3.4 BIOS will start updating
Note: Please DO NOT shutdown or restart system until BIOS update process is completed.
Note: Please also note that Mouse and Keyboard would be locked during updating.

## Slide 10: Step 4. Check BIOS version after update Completed
4.1 After BIOS update is finished, the system will automatically restart. Enter to BIOS menu to check updated BIOS version
4.2 Check the Microcode in \SettingsSystem Status of BIOS Advanced mode

## Slide 11: Corsair One i500 BIOS Release History
FW Version | Description
MC4 | MP Release
MC9 | Integrated Microcode 0x125 Integrated Intel ME FW V16.1.30.2361
MCA | Integrated Microcode 0x129
MCB | Integrated Microcode 0x12B